VERIFITS

    A Program to verify that a FITS file conforms to the FITS Standard.

       
DESCRIPTION

    This task reads a FITS file and verifies that the header and data in
    the  primary array and in every extension conform to the FITS format
    standard.  It first reads the required header keywords checking that
    they  are  in  the correct order and have legal values. Then all the
    remaining header keywords are read to verify that  they  conform  to
    the  FITS  syntax rules.  Optionally, all the header keywords may be
    printed out.  A warning message is printed if any duplicate keywords
    (except  for  COMMENT,  and  HISTORY)  are found.  Finally, any fill 
    characters after  the  END  keyword are checked to be sure that they 
    are all blanks (ASCII 32).
    
    If  requested to do so, then VERIFITS next attempts to read
    all the data values.  For primary arrays  and  image  extensions  it
    computes  and  displays  the mininum and maximum data value and also
    counts the number of pixels that are undefined  (i.e.,  are  set  to
    the  null  value).   For Random Group FITS files this information is
    calculated for each group separately.  For  ASCII  or  binary  table
    extensions,  each  column  is  read individually and the minimum and
    maximum values and the number of undefined values are calculated.
    
    Finally, VERIFITS checks that any fill bytes at the end of  the  data
    have  a  valid  value (i.e., must equal zero except for ASCII tables
    which must be filled with ASCII blanks).  Each extension is  checked
    in turn, until the end of file is reached.
    
    VERIFITS  prints  a  summary  table showing the structure of the FITS
    file and a description of any errors  that  it  finds.   Optionally,
    all the header keywords may also be printed.
    
    VERIFITS  supports  all  standard types of FITS files and extensions,
    including:  primary  arrays,  random groups, image extensions, ASCII
    TABLE   extensions,   and  BINTABLE  extensions.    Within  BINTABLE 
    extensions,  both  fixed-length  and  variable-length vector columns
    can be verified.
    
PARAMETERS

    VERIFITS asks the user for 4 input parameters when it is run:

   1 Input file name.  This is the name of the FITS file to be verified.
    
   2 Optional output file name to write the verification report.  The
     default is to print the report to standard output on the user's teminal.

   3 Should the header keywords be printed? (default = yes)
    
   4 Should  every  data  value  be  read and verified?  (default = yes)
     Answering 'No' will increase the execution speed of the task  at
     the  expense  of  doing a less rigorous verification of the FITS
     file.