## Slide 1: Antennas and Receivers in Radio Astronomy
Todd Hunter (NRAO Charlottesville)

## Slide 2: Outline: Following the Signal Path
Antennas:
  Shapes, efficiencies, primary beam response, holography
  Pointing, tracking, and servo systems
  Polarization
Receivers:
  Amplifiers & Mixers
  Local oscillators
    Phase lock loop
    Modulation (Walsh functions and sideband separation)
  Sensitivity
    Receiver temperature
    Derivation of radiometer equation

## Slide 3: Role of an antenna
Track and capture radiation from an object over a broad collecting area and efficiently couple it into a receiver so that it can be detected, digitized, and analyzed.
Example:
  100m GBT operating at 90GHz
  WR-10 waveguide: 2.54 mm
  Physical reduction: 40000x
An aside: What the heck is a dB (decibel)?
Expression of the relative strength of two signals
  A change of 3dB = 2x (-3dB = 0.5x)
  A change of 10dB = 10x (-10dB = 0.1x)
  A change of 20dB = 100x (-20dB = 0.01x)

## Slide 4: Importance of Antenna properties on your data
Antenna amplitude and phase patterns cause amplitude and phase to vary across the field of view.
Polarization properties of the antenna modify the apparent polarization of the source.
Antenna pointing errors cause time varying amplitude and phase errors.
Variation in noise pickup from the ground can cause time-variable amplitude errors.
Deformations of the antenna surface can cause amplitude and phase errors, especially at short wavelengths.

## Slide 5: Antenna shapes
Horn antennas
  Advantage: Broad bandwidth
  Large apertures not practical,
  (long, cannot be close-packed)
Reflector dish antennas
  Advantage: large apertures, homology (von Hoerner 1967)
  Disadvantage: Require many feeds,
  each of limited bandwidth
Dipole (wire) antennas
  Examples: LWA, LOFAR low-band
  Advantage: wide field, beam-forming
  Disadvantage: low gain, need 1000s
Purcell horn: HI (1951)
Crawford Hill horn
reflector: CMB (1965)
GBT feeds
LWA
antenna
VLA

## Slide 6: Reflector antennas
Prime Focus
GMRT
GBT
VLA,
ALMA
SMA
ATCA,
Mopra
CARMA,
CSO
Offset Cassegrain
On-axis Cassegrain
Dual offset Gregorian
Bent Nasmyth
Nasmyth
Cleanest beam, minimizes standing waves, polarization asymmetry compensated -- Mizugutch et al. (1976)
Receivers do not tilt in elev.
(best for array receivers)

## Slide 7: Reflector antenna efficiencies
Response pattern (primary beam): A(n,q,f) = A(n,q,f)/A0
Effective area (on-axis): A0=hA=(aperture efficiency)(pR2)
where h = hsurfacehblockagehspilloverhtaperhradiationhmisc
hsurface = exp(-(4ps/l)2) s = rms surface error (Ruze 1966)
  = 0.44 for s = l/14 (VLA at 43 GHz) sVLA~500mm
  = 0.79 for s = l/26 (VLA at 22 GHz) sALMA~25mm
hblockage = blockage efficiency (feed legs and subreflector)
hspillover = feed spillover efficiency
htaper = feed taper efficiency
hradiation = metal reflection efficiency (~0.99 per Al mirror)
hmisc= diffraction, phase, focus error, polarization efficiencies
s
} hillumination=0.8 for -10dB taper

## Slide 8: Comparison of primary beam response
in radians,
l and D in the same units
Set by the illumination taper of the receiver feed,
i.e how much of the outer part of the dish are we using?
Fourier transform pairs

## Slide 9: Uniform Antenna illumination: VLA
              Shaped symmetric primary, shaped asymmetric secondary
              Close to Airy disk (FWHM~1.028 λ/D) (radius of 1st null=1.22 λ/D)
              Better illumination efficiency (90%) at expense of higher sidelobes (-16 dB)
              CASA model: Airy truncated at 10%

## Slide 10: Tapered Antenna illumination: ALMA
also SMA, CARMA, etc.
  Paraboloidal primary
  Hyperboloidal secondary
  -10dB taper: good compromise between efficiency and sidelobes
  Illumination efficiency ~ 80%
  Low sidelobes (-23 dB)
  Larger beam: θFWHM = 1.13 λ/D
  Baars* (2007) and ALMA Memo 456 give numerical formulas relating FWHM to taper:
    τ = 10^(taper/20)
    θFWHM=(1.243 – 0.343τ + 0.12τ2) λ/D
*The Paraboloidal Reflector Antenna in Radio Astronomy and Communication

## Slide 11: Holography is a vital tool
The technique of imaging the (complex) beam pattern of an antenna and Fourier transforming back to the antenna surface illumination (aperture plane) is known as “holography”. (Napier & Bates 1971, Bennett et al. 1976).
Interferometric holography is done with a beacon transmitter on a tower, or on a satellite, but can also be done on bright quasars, which is called “astroholography” or “celestial holography”.
Non-interferometric holography, also called “out-of-focus (OOF)” or “phase retrieval”, is useful for measuring large-scale surface error
Holography allows us to measure:
Antenna panel misalignment (e.g. ALMA: Baars et al. 2007, IEEE A&PM)
Systematic antenna panel mold error (GBT: Hunter et al. 2011, PASP)
Large-scale error due to thermal effects (GBT: Nikolic et al. 2007, A&A)
Illumination pattern alignment errors (see ALMA Memo 402)
Effect of feed legs on the beam

## Slide 12: Holography principle
Reference antenna
Antenna(s) under test
θ
Record a 2D image of complex voltage pattern V(θ, θ’)
V(θ,θ’) = Σ exp[i(ψx(θ,θ’)-ψy(θ,θ’))]
x,y

## Slide 13: What do holography data look like?
Example:
SMA at 232 GHz
Amplitude
Phase
Beam map (angle units)
Aperture map (distance units)
Fourier transform
ELEVATION
ELEVATION
AZIMUTH

## Slide 14: Holography: ALMA surface panel adjustment
Before adjustment (43mm)
After adjustment (11mm)
Phase map converted to path length error from ideal paraboloid

## Slide 15: Holography: Effect of feed legs on beam
in radians,
l and D in the same units
Vertex NA ALMA Antenna
AEC ALMA Antenna
Feedlegs block and scatter radiation prior to reaching the primary
In some cases, they also block the path back up to the subreflector
Sidelobe pattern rotates w.r.t. celestial objects: parallactic angle coverage needed for proper polarization calibration
Focus errors cause beam asymmetry

## Slide 16: Front End polarization separation
in radians,
l and D in the same units
For optimal sensitivity, we want dual-polarization receivers
Two types of devices can provide ~20dB purity with low loss:
1) Waveguide (i.e. after the feed): Ortho-Mode Transducers (OMTs)
  Can be designed numerically (Maxwell’s eqs.)
  Easy to machine when large (i.e. low frequency)
2) Quasioptical (i.e. in front of feed): Wire grid
Advantage: easier to construct for high freq.
Disadvantage: Alignment tricky (“squint” ~θ/10)
VLA S-band (2-4 GHz)
ALMA Band 3 OMT Band 6 OMT (opened)
Pol 1
Pol 0

## Slide 17: Polarization separation: ALMA Band 7 grid
in radians,
l and D in the same units
LO
IF
High frequencies: wire grid
  Reflects one linear polarization, passes the other
  Wire diameters of ~ 10 microns, fairly easy to wind
  Two feedhorns instead of one

## Slide 18: ALMA Cross-polarization patterns
Band 3 (100 GHz):
Co-polarization pattern
Off-axis cross-polarization pattern (“clover leaf”)

## Slide 19: Antenna thermal effects and metrology
Thermal gradient in antenna structure affect the focus, pointing and surface accuracy of antennas  point/focus more often during the day
Performance is generally best during second half of the night when temperature has stabilized and dish has “relaxed”
Some telescopes use “thermal terms” in their focus and/or pointing models using thermometers: e.g. IRAM 30m, GBT
Metrology devices: inclinometers to measure tilts (e.g. GBT, ALMA)
ALMA

## Slide 20: Antenna gain curve
Best efficiency is usually tuned to intermediate elevations
Gravity distortions increase away from this point
Similar curves for VLA are available in CASA
IRAM 30m (predicted, 1999)

## Slide 21: Antenna pointing and tracking
in radians,
l and D in the same units
Static errors: Blind pointing vs. offset pointing
ALMA: blind=2”, offset=0.6” rms (θFWHM/10 at Band 10)
VLA: blind~15”, offset=3” rms (θFWHM/17 at 50 GHz)
Dynamic errors: wind etc.
VLA: tracking ~ 3” rms (no wind)
i.e. peak excursions +-6”
θFWHM/10 at 43 GHz
How good is θFWHM / 10 ?
not very good away from
the beam center!

## Slide 22: Antennas: How do they slew & track?
RA = 17:20:53.5
Dec = -35:47:00.0
LST = 15:43:12
Latitude = -23.0229
Longitude = -67.7549
Elevation = 5040m
Azimuth angle & velocity
Elevation angle & velocity
Servo system

## Slide 23: Antenna Az/El servo loop overview
in radians,
l and D in the same units
Input parameters
  Commanded position & tracking velocities (~5 Hz)
  Pointing model: converts topocentric Az/El to actual Az/El
Multiple nested servo loops (software/firmware)
  Position loop (~5 Hz): Encoder: converts angular position of antenna axis to integer
    Velocity loop (~100 Hz) Tachometer: converts motor shaft angular velocity to voltage
      Motor current (torque) loop (~ a few kHz) Resolver: converts motor shaft angle to voltage or integer
Position command
Motor Torque command
Velocity command

## Slide 24: Detail of velocity servo loop: PID type proportional / integral / derivative
Commanded
velocity
Actual
velocity
Error
Velocity
Motor
Amplifier
The gains must be tuned for each loop: Kpos, Kinteg, Kderiv

## Slide 25: System response vs. gain
Trade-off between reducing overshoot and reducing oscillation frequency to below the antenna’s lowest resonant frequency
Servo systems use many hardware and software safety checks to avoid runaway conditions or damage.
VLA is currently revitalizing it servo system with modern components
Time (seconds)

## Slide 26: Role of an receiver
Linearly amplify weak RF signals while adding minimal noise, and downconvert them to room-temperature output signals at a few GHz (called “IFs”) on coax cables suitable for digitization
Receivers are often called “Front Ends” or FE

## Slide 27: VLA receiver summary
Q
Ka
K
Ku
X
C
S
L
Letter designations have historical context and are second nature to microwave engineers.
S
L
C
X
Ka
Q
K
Ku
Offset Cassegrain Feed Circle
Wavelength Band (letter code) | Nominal frequency range (GHz) | Polarization, operating temperature
4 m (4) | .058-.084 | Linear, 300K
90 cm (P) | 0.23-0.47 | Linear, 300K
20 cm (L) | 1.0-2.0 | Circular, 15K
13 cm (S) | 2.0-4.0 | Circular, 15K
6 cm (C) | 4.0-8.0 | Circular, 15K
3 cm (X) | 8.0-12.0 | Circular, 15K
2 cm (Ku) | 12.0-18.0 | Circular, 15K
1.3 cm (K) | 18.0-26.5 | Circular, 15K
1 cm (Ka) | 26.5-40.0 | Circular, 15K
0.7 cm (Q) | 40.0-50.0 | Circular, 15K

## Slide 28: ALMA receiver summary (dual linear pol.)
Q
Ka
K
Ku
X
C
S
L
Letter designations have historical context and are second nature to microwave engineers.
Band (number code) | Frequency range (GHz) | Sidebands, Polarization splitter
7 mm (1) | 32-50* | SSB, OMT*
4 mm (2) | 67-90* | ?SB, OMT*
3 mm (3) | 84-116 | 2SB, OMT
2 mm (4) | 125-163 | 2SB, OMT
1.6 mm (5) | 163-211 | 2SB, OMT
1.3 mm (6) | 211-275 | 2SB, OMT
0.9 mm (7) | 275-373 | 2SB, Wire grid
0.7 mm (8) | 373-500 | 2SB, OMT
0.45 mm (9) | 600-720 | DSB, Wire grid
0.35mm (10) | 787-950 | DSB, Wire grid
* under development
Band 1
2
3
4
5
7
6
10
9
8

## Slide 29: Overview of Receivers and IF systems
Three basic technological limitations dictate what we do:
  We can build good amplifiers up to ~100 GHz
  We can digitize signals of bandwidth up to ~2 GHz
     to observe at >100 GHz, the front-end must be a mixer
     to observe a bandwidth >2 GHz, you need a mixer in the IF chain
  Mixers and amplifiers must be cold when used as the front-end
      Cold amplifiers need ~15K (2-stage cryo)
      SIS mixers need 4K (3-stage cryo)
  So:
  ALMA FE needs cold mixers & amplifiers
  JVLA FE needs cold amplifiers
  Both also require room temperature mixers
  & amplifiers (prior to digitization)
  Mixers are key devices!
Mixer
Amplifier
Coldest Warmest
Mixer

## Slide 30: Amplifiers and mixers
Let’s compare an amplifier and a mixer:
  Amplifiers are 2-port devices: one input and one output
IN
OUT (10-30dB stronger, same frequency)
in radians,
l and D in the same units
Example: NRAO Cryogenic Low Noise Amplifiers (LNAs) using Heterostructure Field Effect Transistors (HFETs) used on the VLA, VLBA, GBT:
Operate at ~15 K
Tnoise ~ 5 hf/k
(i.e. 5 x quantum limit)
M. Pospieszalski (2012)
(MIKON conference)

## Slide 31: What is a mixer?
in radians,
l and D in the same units
LO = Local Oscillator
RF input
= “Radio”
Frequency
IF output =
Intermediate Freq.
ΦIF = ΦRF
LO
uLSB
uUSB
uIF
  Mixers are 3-port devices: LO and RF inputs, and IF output.
  Invented around WWI for radio direction finding (see IEEE Microwave Magazine Sept. 2013 special issue).
  They multiply the LO & RF signals and transfer the phase from the RF to the IF by “heterodyning”. Typically the IF contains signals from two sidebands.
  They are key components for interferometers!!

## Slide 32: Different Kinds of Mixers
in radians,
l and D in the same units
Delicate, cryogenic SIS junctions mixers used as FE
SIS = Superconductor – Insulator – Superconductor
First astronomical use: Dolan, Phillips & Woody (1979)
Theory: Tucker (1979)
SMA 650 GHz mixer block (Nb/AlOx) with feedhorn (for LO and RF input)
Image of SIS junction from
Electron Microscope (Hedden et al. 2010)
80 micron
S I S
Area ~ 1 square micron
Inexpensive Off-the-Shelf room temperature mixers:
Used in IF circuitry after the received signal has been sufficiently amplified

## Slide 33: Sidebands
Receiver design options: SSB, 2SB, 1SB, DSB
SSB: the RF signal is filtered so that only one SB emerges from the mixer
  Examples: VLA receivers
2SB: the mixer separates the two SBs with a 90° hybrid quadrature coupler. Rejects signal and atmospheric noise of the image SB by 10-20 dB
  Examples: ALMA Bands 3 – 8,
1SB: a 2SB system where one SB output is simply terminated (i.e. unused)
  Examples: ALMA Band 2 NA prototype
DSB: both sidebands are superposed on one another
  Examples: ALMA Bands 9-10, SMA
  Requires 90 deg Walsh modulation on the LO
  to separate them (but only for inteferometry)

## Slide 34: SSB: VLA receivers
Freq
(GHz)
Ka-Band Rx
26-40 GHz
IF Out
8-18 GHz
8
12
16
20
24
28
32
36
40
44
48
52
4
0
56
60
LO = 46 GHz
28-38 GHz
Power
(dBm)
2SB: ALMA Bands 3-8
LSB
2 pols
USB
2 pols
LO = 341 GHz
Band 7: Meier et al 2005

## Slide 35: Local oscillators
Goal: Deliver stable, accurate phase reference to a remote mixer
Problem: Signals lose S/N upon transmission, and must be “cleaned up”
Phase lock loop (PLL) circuit is analogous to an antenna drive servo
Compares phase of two signals, correcting at BW ~ 1 MHz
Frequency
Intensity (dBm)
Intensity (dBm)
Unlocked
Locked
ALMA YIG oscillator
Loop BW

## Slide 36: LO Modulation: Walsh switching
See Thompson, Moran &
Swenson (chapter 7);
ALMA Memo 586
Impose on LO
Remove in correlator
180 degree Walsh switching
  Suppresses spurious signals (birdies) that arise between the frontend and the digitizer
90 degree Walsh switching
  Allows you to separate sidebands in cross-correlation
  Will double the bandwidth for DSB receivers (Bands 9-10)
LO Offsetting (see ALMA Memo 287)
  Suppresses the opposite sideband (by moving its fringe to several kHz and letting it “wash” out)
  Suppresses spurious signals, but does not reduce broadband noise
Phase
Time

## Slide 37
Good receiver systems have a linear response:
Vout
Tinput
Tcold
Thot
Vrx +Vcold
Vrx + Vhot
-Trx
To measure Trx, you need measurements of two calibrated ‘loads’. In the lab, you use:
Tcold = 77 K liquid nitrogen load
Thot = Room temperature load
Power(n) 
 Voltage
Power detector P  V
Unknown slope
Calibrated ‘load’
Receiver temperature
Starting from
Define the
“Y” factor
Sensitivity: Trx and the Temperature Scale

## Slide 38: ALMA Sensitivity: Band 6 (230 GHz)
TRX: receiver sensitivity
TSYS: system sensitivity
O3 line
Autocorrelation spectra from Tsys scan
Note 3dB IF power variation vs. freq
Shape is removed from cross-correlation

## Slide 39: T(Rx) vs. Frequency for JVLA Receiver Bands
Chart: Frequency (GHz)
L-Band 1-2 GHz | 21.9999 | 15.5914 | 12.3695 | 10.8072 | 9.2728 | 8.9591 | 9.0934 | 9.3219 | 9.0968 | 10.1486 | 12.2069
S-Band 2-4 GHz | 19.5905 | 16.8951 | 19.5905 | 11.7715 | 15.7049 | 12.8 | 14.492 | 12.2806 | 11.7085 | 12.2164 | 12.8 | 11.2107 | 12.2806 | 12.8 | 12.2806 | 12.2806 | 14.492 | 13.3299 | 12.8 | 14.492 | 15.7049
C-Band 4-8 GHz | 15.8 | 10.1 | 8.76 | 8.17 | 7.41 | 7.57 | 8.76 | 7.56 | 8.07 | 6.8 | 6.12 | 6.99 | 7.15 | 9.02 | 7.24 | 6.02 | 6.36 | 5.7 | 7.58 | 9.48 | 8.54 | 4.68 | 7.13 | 5.86 | 7.47 | 9.23 | 7.66 | 6.61 | 7.51 | 7.86 | 7.43 | 7.48 | 6.71 | 7.46 | 9.45 | 9.79 | 7.75 | 8.46 | 7.79 | 9.92 | 9.9
X-Band 8-12 GHz | 11 | 10.5 | 10.2 | 9.7 | 8.7 | 8.5 | 8.4 | 8.4 | 8.7 | 8.1 | 8.4 | 8.1 | 8.6 | 8.2 | 8.1 | 8.2 | 8.5 | 8.3 | 8.5 | 8.5 | 7.4 | 6.9 | 8.1 | 8.7 | 8.5 | 8 | 7.3 | 6.8 | 7.3 | 8.1 | 7.8 | 7.3 | 7 | 7.4 | 7.3 | 7.9 | 7.8 | 8.6 | 8.7 | 9.5 | 10
Original EVLA Project Book - TRx Requirements (Band Center) |  |  |  |  |  |  |  | 
Band | L | S | C | X | Ku | K | Ka | Q
TRx | 14 | 15 | 16 | 20 | 25 | 34 | 40 | 48

## Slide 40: Radiometer equation derivation & simulation
Consider a sample time series of an RF signal: xn ~ N (mean=0, variance=σ2)
Normalize it by its standard deviation: Zn = xn / σ , xn =σZn
Square this to get the power: Zn 2 =χ2(1) is the Chi square distribution with 1 d.o.f.
xn2 = σ2 Zn 2 = Γ(1/2 , 2σ2) = the gamma distribution (c.f. constant * Chi square)
with expectation mean = μgamma = σ2, and expectation variance =σ2gamma = 2σ4

## Slide 41: Radiometer equation derivation
5. The Nyquist sample rate is twice the bandwidth (2β) and the time interval of the data is τ, making the number of statistically independent samples N = 2βτ
The Standard Error of the Mean* states that the sample power as computed from (1/N) Σxn2 will have a distribution variance of σ2p = 2σ4/N = 2σ4/ (2βτ) = σ4/ (βτ) and thus its standard deviation is σp = σ2 / √(βτ)
Substitute μgamma (from Step 4) for σ2 in the numerator: σp = μgamma / √(βτ)
  NOTE: μgamma is the expectation mean of xn2 and is equivalent to the sample mean power P for large N. This gives: σp = P / √(βτ)
8. Radiometer output power in RJ limit is: P = k TβG (where G = gain)
Thus, σp /P = σT /T and σT = T / √(βτ) independent of Gain!
(*e.g. Casella & Berger 2002)
Recall the input power level was 4!

## Slide 42: Conclusions and Further reading
For more information on ALMA antennas, receivers, and correlators, see the ALMA Technical Handbook at http://almascience.org
Also, see my ADS Private Library on ALMA technology:
  http://adsabs.harvard.edu/cgi-bin/nph-abs_connect?library&libname=ALMA+technology&libid=464295c89a
And my ADS Private Library on holography: libname=Holography&libid=464295c89a
For more info on EVLA receivers: http://www.aoc.nrao.edu/~pharden/fe/fe.htm
Knowing a bit about the signal path can really help you understand your data, especially when there are problems or caveats (such as just how good is that primary beam correction?)

## Slide 43: Extra Slides

## Slide 44: Example: SMA antenna servo Three nested loops
1. Antenna position loop ~ 5 Hz
2. Motor velocity loop ~ 100 Hz
3. Motor current loop ~ few kHz
Micro-
controller
board
DAC
ADC
Position and
Velocity request
Motor
Limit switches
Tachometer

## Slide 45: Safety is #1 priority
Hardware
Limit switches, 2 per direction per axis
Hardstops must decelerate antenna from Vmax without destroying antenna
Loss of power should cause brakes to engage (i.e. power holds them open)
Applying brakes at full speed should not destroy antenna
Manual E-stop switches prominent, with no Silicon in the circuit
Watchdog timer: if microcontroller fails to clear it every few ms, engage E-stop
Philosophy: if any wire breaks, system should stop as gracefully as possible
Software:
Software limit switches
Microcontroller must deactivate motors & apply brakes if:
  encoder stops sending data, or antenna computer stops sending new values
  tachometer reports overspeed, or differs from encoder derivative
  Any large oscillation is detected

## Slide 46: ALMA Receivers (dual linear polarization)
Lens, OMT
Band 4
125-163
Band 6
211-275
Band 7
275-373
Band 8
385-500
Band 9
600-720 GHz
OMT
OMT
Wire grid
OMT
Wire grid
Band 3
84-116

## Slide 47: Rogues Gallery of (Naked) JVLA Receivers
http://www.aoc.nrao.edu/~pharden/fe/fe.htm
L
S
X
Ku
K
Q
C
A
World’s best LNA’s from CDL
1-2 GHz
2-4
4-8
8-12
12-18
40-50
18-26
26-40

## Slide 48: Holography: effect of GBT panel mold error
Panel size ~2m, error beam ~50 θFWHM

## Slide 49: Holography: measuring and correcting the daytime distortion of GBT

## Slide 50: ALMA Block Diagram
4K SIS mixer
300K analog
mixer
Digital mixer

## Slide 51: SIS mixer I/V curve
in radians,
l and D in the same units
1. Resistor: Ohm’s law
2. Diode: Shockley’s law
“Non-linear” device
3. SIS tunneling junction:
superconducting
normal
I=0 below gap voltage
Photons can break Cooper pairs of electrons and create tunneling current
230 GHz = 0.8 meV
Vgap(Nb) ~2.9mV
Vbias ~ 2.5mV
fgap(Nb)=(Vgap)e/h=700 GHz
f>fgap degrades Trx
Requires T < 5 K
Vbias

## Slide 52: Digitizers and Nyquist zones
in radians,
l and D in the same units
Anti-aliasing bandpass filters are essential to prevent leakage from adjacent Nyquist zones.
Nyquist theory:
Fsample >= 2*Bandwidth
ALMA & VLA sample
in Nyquist Zone 2:
ALMA: 2-4 GHz (4.0 Gsample/sec) x 4 of them x 2 pols
JVLA: 1-2 GHz (2.048 Gsample/sec, 8-bit digitizers) x 2 of them x 2 pols
2-4 GHz (4.096 Gsample/sec, 3-bit digitizers) x 4 of them x 2 pols

## Slide 53: Measurement of Tsys in the Sub(millimeter)
Power is really observed but is  T in the R-J limit
Tsys = Tload * Tout / (Tin – Tout)
Vin = G Tin = G [Trx + Tload]
Vout = G Tout = G [Trx + Tatm(1-e-t) + Tbge-t + Tsourcee-t ]
SMA calibration load swings in and out of beam
Load in
Load out
If Tatm ≈ Tload, and Tsys is measured often, changes in mean atmospheric absorption are corrected. ALMA has a two temperature load system which allows a measure of Trx
The “chopper wheel” method: putting an ambient temperature load (Tload) in front of the receiver and measuring the resulting power compared to power when observing sky Tatm (Penzias & Burrus 1973).
Vin – Vout Tload
Vout Tsys
=
Comparing in and out
assume Tatm ≈ Tload

## Slide 54
ALMA